Model:  PS-B

Description:  Family of three different power supplies for use with different radio components.

Basic model is a PS-B-200 which is a 200 watt power supply that converts 115VAC to +13.8VDC.  This unit is suitable to connect to several different types of radios depending on the cable you connect to it.  You will be able to power your older M15, or the Newer M2115 radios.

The next size up in power is the PS-B-320.  This is a 320 watt power supply which will convert 115VAC or 230VAC to  +28VDC.  This power supply is suitable for connecting to your MB-R radio.  This allows your older M15 to power the newer PA-25 power amp.

The largest power supply is the PS-B-450.  This is a 450 watt power supply to allow upgrading the new M2115-B base radio for use with a 50 watt external radio frequency power amplifier.

| Model | Input Power | Output Voltage (+ VDC) | Output Power (Watts) | NOTE | Used with |
| --- | --- | --- | --- | --- | --- |
| PS-B | 115VAC | 13.8 | 200 |  | M2115-M |
| PS-B-200 | Same as | 13.8 | 200 |  | M2115-M |
| PS-B-320 | 88-264VAC | 28 | 320 |  | MB-R, M15-25, PA-25-E |
| PS-B-450 | 90-130VAC or 180-264VAC (switch selectable) | 28 | 450 | 2 | MB-R-50, M15-50 |

Notes:

- M2115-M is the mobile version M2115.

- M15-50 is the M15-25 with the 25W amp replaced with a 50W power amplifier.

All units look the same. Only output power and voltage are different.

Dimensions:  9.6”x 7.6”x3.2”.

*** following not for marketing – FYI ONLY ****

To upgrade from using power supply with an external power amp to using with a radio remove top cover, attach radio base and install new top cover. Both the older M15 and a PA25 or a new M2115 may be connected to the same base.